## Slide 1: Preliminary Screening Of Raw Propolis Sample As Pre-formulation Study For Topical Preparations
Presented by: Ghaida Mustafa
PhD researcher, CPES, University of Bradford, UK
Supervisors: Prof. Anant Paradkar, Dr. David Ansel and Dr. Shahzeb Khan
Life Sciences PGR Conference 2024

## Slide 2: Contents
Background.
Aim of the study.
Method.
Results and discussion.
Conclusion.
Acknowledgment.
References.
Life Sciences PGR Conference 2024

## Slide 3
Mummification
Beautification
Glue
Sealer

## Slide 4: Background
Propolis is a natural bee haemostat.
Numerous biological activities.
Phenolic acids and flavonoids.
Chemical composition variation.
Life Sciences PGR Conference 2024

## Slide 5
Life Sciences PGR Conference 2024
Propolis with valuable Biological activities on Skin
Wound healing
UV absorption
Antiaging

## Slide 6: https://www.who.int/health-topics/leishmaniasis#tab=tab_1 https://doi.org/10.1007/s00436-008-0970-z
‘’Greater imitator’’
~ 1 million new cases & 30,000 deaths /year.
Propolis
Propolis nano formulations
Topical application

## Slide 7: Aim of the study
To analyse raw propolis sample from India as topical preparations pre-formulation assay using Thermal gravimetric analysis (TGA), Fourier Transform Infrared (FTIR) and Reverse phase high performance chromatography (RP-HPLC).
Life Sciences PGR Conference 2024

## Slide 8: Method
TGA:
Heating program: in the presence of air at flow rate of 25 ml/min from room temperature to 105 °C at 10 °C/min, isothermal for 30 min. Heating at 10 °C/min to 550 °C, holding temperature for 30 min.
Life Sciences PGR Conference 2024

## Slide 9: Method
2. FTIR:
Measurement: PerkinElmer Frontier FT-IR spectrometer.
64 Scans were performed from 4000-650cm-1.
Life Sciences PGR Conference 2024

## Slide 10: Method
3. RP-HPLC:
HPLC system: Waters e2695 separation module Waters 2998 Photo diode array (PDA) detector and Empower software Application.
Column: Waters Symmetry 300 TM, C18 (250x4.6 mm, i.d., 5µm).
Gradient mobile phases: 0.1% formic acid (solvent A) and methanol (solvent B) at a flow rate 1ml/min and 10 minutes condition column between the runs.
The chromatograms were collected at 290 nm.
Life Sciences PGR Conference 2024

## Slide 11: Results
1. TGA:
Life Sciences PGR Conference 2024

## Slide 12: Results
2. FTIR:
Life Sciences PGR Conference 2024
FTIR spectrum of raw Indian propolis sample showing bands related to wax (red colour) and phenolics compounds (green colour).

## Slide 13: Results
3. RP-HPLC:
Life Sciences PGR Conference 2024
Chromatogram for standard references: 1. Chlorogenic acid, 2. Caffeic acid, 3. Ferulic acid, 4. Rutein, 5. Cinnamic acid, 6. Pinocembrin, 7. Chrysin, and 8. Galangin.
Chromatogram of raw Indian propolis sample: 1. Chlorogenic acid, 3. Ferulic acid, 5. Cinnamic acid, 6. Pinocembrin, 7. Chrysin, and 8. Galangin.

## Slide 14: Conclusion
Life Sciences PGR Conference 2024
Data from the current study will provide a standardized profile of the analysed raw propolis samples, offer an initial guidance in the rational selection of the propolis formulation technique and allow the monitoring of the desired compounds for topical formulations.
Propolis topical preparations

## Slide 15: Acknowledgment
Life Sciences PGR Conference 2024

## Slide 16: References
Life Sciences PGR Conference 2024
Herrera-López MG, Richomme P, Peña-Rodríguez LM, Calvo-Irabien LM. Bee species, botanical sources and the chemical composition of propolis from Yucatan, Mexico. Journal of Chemical Ecology. 2023 Aug;49(7):408-17.
Bensharada M, Telford R, Stern B, Gaffney V. Loss on ignition vs. thermogravimetric analysis: A comparative study to determine organic matter and carbonate content in sediments. Journal of Paleolimnology. 2022 Feb 1:1-7.
Miłek M, Ciszkowicz E, Zaguła G, Grabek-Lejko D, Pasternakiewicz A, Lecka-Szlachta K, Dżugan M. Quality of Propolis Commercially Available on Podkarpacki Beekeeping Market. Journal of Apicultural Science.
Touzani S, Imtara H, Katekhaye S, Mechchate H, Ouassou H, Alqahtani AS, Noman OM, Nasr FA, Fearnley H, Fearnley J, Paradkar A. Determination of phenolic compounds in various propolis samples collected from an African and an Asian region and their impact on antioxidant and antibacterial activities. Molecules. 2021 Jul 29;26(15):4589.

## Slide 17
Thank you